## Slide 1
Demo on FPGA PC communication
March 8,2014

## Slide 2: Important Files for this Demo
makestuff-windows-20130719
libfpgalink-20120621.tar
libusb-win32-bin-1.2.6.0
[ Console-2.00b148-Beta_32bit ]
[ Microsoft Visual Studio ]

## Slide 3: Steps for Working environment setup Demo
Download and install Visual C++ Express 2010
http://www.microsoft.com/visualstudio/en-us/products/2010- editions/express#Visual_Studio_2010_Express_Downloads
2. Download and install Microsoft Visual C++ 2010 Redistributable Package (x86)
http://www.microsoft.com/en-us/download/details.aspx?id=5555
Download "Build Infrastructure", windows version. This is the environment where we’ll work with the FPGALink library binaries.
http://www.makestuff.eu/wordpress/software/build-infrastructure/
On windows, unpack the downloaded archive
makestuff-win32-20111211.zip in your own directory.
In my case, I did this directly in C:\. This created C:\makestuff\.

## Slide 4
4. Download the latest FPGALink library binaries (at the time of writing this lab, the latest version is "libfpgalink-20120621.tar.gz"
http://www.makestuff.eu/wordpress/software/fpgalink/
Unpack it in C:\makestuff\libs\
5. Download and install "Console 2".
http://sourceforge.net/projects/console
unpack the downloaded archive directly in C:\Program Files\
5.1 Create shortcut to C:\Program Files\Console2\Console.exe
5.2 Launch Console 2 and enter C:\makestuff\msys\bin\sh.exe --login in the "Shell" and C:\makestuff\ in startup dir box at Edit->Settings->Console

## Slide 5
6. Download “LibUSB-Win32”. http://sourceforge.net/projects/libusb-win32/
Plug in the Atlys board and turn the power on. Then run bin/inf-wizard.exe. Click “Next”, select your FPGA board, make a note (in our case, the Atlys board, that is 1443, 0007) of the vendor and product IDs and click “Next” twice. Choose a location for the driver and click “Save”. Click “Install Now”.

## Slide 6: VHDL coding and .xsvf programming file generation
Create ISE project suppose “Lab8”. Now add Copy of Source .
Files List
top_level.vhdl
comm_fpga_fx2.vhdl and
top_level.ucf

## Slide 7: 2. Create a .bit by double click on Generate Programming File

## Slide 8
3. Creating .xsvf file
Inside ISE project Navigator, select Tools->iMPACT. The ISE iMPACT window should pop-up after a few seconds.
Double click on “Boundary Scan” and then right click at the white space as in the picture in the next slide and follow the picture

## Slide 9
Now give the file name and the directory where your xsvf
file to be saved then click save

## Slide 10
When you click Ok it will redirect you to select the .bit file
you already generate on slide 6

## Slide 11
Select Your .bit file and click Open

## Slide 12
Now select the chip and right click then program then
on the coming window select the deice and click ok
Now you have done all , copy the .xsvf file to the directory
C:\makestuff\libs\gen_xsvf Note: new folder gen_xsvf

## Slide 13: Testing and validation of the overall host-FPGA system
--Connect and power-on the Atlys board if not already.
--Start a terminal by launching Console 2. We’ll use the flcli utility on the host side.
--Use flcli utility to program the FPGA. In the Console 2 terminal, do:
> cd libs/libfpgalink-20120621
> ./win32/rel/flcli -v 1443:0007 -i 1443:0007 -s -x gen_xsvf/mydemo.xsvf

## Slide 14
--Use flcli utility to connect to the FPGALink device 1443:0007 (that is the USB controller on the Atlys board):
> ./win32/rel/flcli -v 1443:0007 -c
Which enters the command-line mode, where we can use the flcli utility’s built-in functions to write and read the registers we have created on the FPGA. For example, try this:
> w0 37
And observe the LEDs on the board
3 | 7 0011 0111 Five LEDs toggle to ON

## Slide 15
read the status of the slide switches:
> r0
Write into R1 and R2:
> w1 02;w2 03
> r1
> r2
> r3
If everything went OK, your Console 2 window should look like in Fig.4.
Quit the flcli utility:
> q

## Slide 16
Thanks